## Slide 1
LHC Beam Energy
J. Wenninger
CERN
Beams Department
Operation group / LHC

## Slide 2: Outline
Beam energy
Beam energy measurements methods
Beam energy measurements at LHC

## Slide 3: Beam momentum - definitions
The deflection angle dq of a particle with charge Ze and momentum P in a magnetic field B(s):
r
dq
ds
Integrated over the circumference:
The momentum is given by the integrated magnet field:
LHC: 1232 14.3m long dipoles, 8.33 T

## Slide 4: Beam momentum
What magnetic fields / magnets contribute to the integral?
In the ideal LHC only the dipoles contribute.
  The absolute error on the LHC dipole field is estimated to be ~ 0.1%.
  (magnet calibration)
In the real LHC the contributions to the integral (typical values) are:
  Dipoles ≥ 99.8%
  Quadrupoles ≤ 0.2%
  Dipole correctors some 0.01%
  Higher multipoles ~0.01% level
For target accuracies of few 0.1%, only the dipoles and quadrupoles matter – the rest can be lumped into the systematic error.

## Slide 5: Circumference and orbit length
The speed bc (and momentum P), RF frequency fRF and length of the orbit L are coupled:
The RF frequency is an integer multiple of the revolution period,
h = 35’640
In the ideal case, the orbit length L matches the circumference C as defined by the magnets, L=C, fRF is matched, the beam is on the design orbit.
What happens if an external force changes the circumference of the ring, or if fRF is not correctly set, such that LC ?
L = C
L > C

## Slide 6: Quadrupoles and circumference
The role quadrupoles in the LHC is to focus the beams. When L=C (on ‘central orbit’) the net bending of the quadrupoles vanishes.
  No effect on the energy.
If LC, the beam is pushed off-axis through quads, giving a net bending in each quad. The energy change can be expressed by:
Strong amplification (for large accelerators)
ac = momentum compaction factor

## Slide 7: LEP classic: Earth tides
Tide bulge of a celestial body
of mass M at a distance d :
q = angle(vertical, celestial body)
Earth tides :
The Moon contributes 2/3,
the Sun 1/3.
NO 12 hour symmetry
(direction of Earth rotation axis).
Not resonance-driven
(unlike Sea tides !).
Accurate predictions possible.
Predicted circumference change

## Slide 8: Moonrise over LEP
11th November 1992 :
The historic LEP
tide experiment !
DC/C = 4x10-8 (DC = 1 mm)
20 Years !!
Energy change at fixed orbit length (fRF)

## Slide 9: Circumference evolution
LHC 2012
To provide energy predictions for every LEP fill, the long-term evolution of the LEP circumference had to be monitored.
  Mainly by observing the beam with position monitors.
It was observed that the LEP/LHC tunnel circumference is subject to seasonal (and reproducible) changes of 2-3 mm.

## Slide 10: Outline
Beam energy
Beam energy measurements methods
Beam energy measurements at LHC

## Slide 11: Polarized beams
Transverse polarization builds up spontaneously due to emission of synchrotron light (asymmetry in the transition probably for the final state spin orientation) – Sokolov-Ternov polarization.
The vertical polarization can reach an asymptotic value of:
The rise-time / build-up time is (r = bending radius):
tST ~ 300 minutes
at LEP (45 GeV)
LEP, 44.7 GeV

## Slide 12: Spin precession
The interest of polarization is that spins precess in magnetic fields.
The number of precession for each machine turn is proportional to the beam energy (a = gyromagnetic anomaly = (g-2)/2):
for electrons
for protons
Recipe for energy measurement:
  Let the beam polarize spontaneously – polarization is a delicate flower that requires a very carefully tuned machine. Many factors destroy it…
  Measure ns !

## Slide 13: Precession frequency measurement
Principle of Resonant Depolarization:
Get a fast transverse magnet.
Sweep the B-field over a narrow frequency range and observe P
If the kicker frequency matches ns, P is rotated away from vertical plane – spin/ flip or depolarization.
LEP example
Very high intrinsic accuracy. LEP standard: ±0.2 MeV / ±4×10-6.

## Slide 14: Polarization with protons?
There is plenty of (visible) synchrotron light at the LHC.
But no spontaneous polarization – the proton is too heavy to make it useful:
gp,LHC = 4’300
ge,LEP = 88’000
= some billion years at LHC
Protons must be polarized at the source, the polarization must be preserved along the accelerator chain (see RHIC) – not at CERN (yet).

## Slide 15: Spectrometers
Momentum measurements using a spectrometer system.
  Requires a well calibrated and monitored dipole.
  Some open drift space on both sides to determine the angles with beam position monitors.
  Spectrometer should be (re-)calibrated at some energies, and used for extrapolation.
  Feasible, but not easy to find a location in the LHC…
LEP spectrometer

## Slide 16: Proton-ion calibration principle (1)
The speed b (and momentum P), RF frequency fRF and circumference C are related to each other:
  The speed bp of the proton beam is related to P:
  An ion of charge Z circulating in the same ring, on the same orbit, has a momentum ZP and a speed bi given by:
1 equation, 2 unknowns (C & b/P)
Provides a 2nd equation:
2 unknowns (C & b/P),
2 measurements (fRF).

## Slide 17: Proton-ion calibration principle (2)
The 2 equations for bp and bi can be solved for the proton momentum P:
Momentum calibration principle:
  Inject protons into the LHC, center the orbit such that L=C (very important !). Measure the RF frequency.
  Repeat for Pb ions.
  The frequency difference Df gives directly the energy.
for Pb82+ m  2.5
 This is the method that we use at the LHC

## Slide 18: Scaling with energy
When ions become very relativistic, the difference wrt protons decreases, vanishing when b = 1 – not good for LHC.
The frequency difference scales  1/P2:
LHC
~4.5 kHz
~20 Hz
Meas. accuracy: ~1 Hz (LEP)
Currently ~3-5 Hz @ LHC
Good for injection
Difficult at 4-7 TeV
~60 Hz
Proton – Lead

## Slide 19: Outline
Beam energy
Beam energy measurements methods
Beam energy measurements at LHC

## Slide 20: LHC p-ion calibration
Presently we have Pb82+ ions to calibrate the momentum at the LHC.
There are 2 modes:
  Comparing p-p with Pb-Pb.
  Using the mixed p-Pb and Pb-p.
Protons – B1
Lead – B2
Orbits of the proton and Pb beams after cogging at 4 TeV (mixed mode), relative to p-p orbit.
Forced on the same RF frequency, LC.
Df is obtained from the radial offsets.
x
4 (mm)
LHC circumference

## Slide 21: Practical details
The measurement of the radial position (or fRF) difference (and therefore of the energy) is dominated by systematic uncertainties related to:
  Reproducibility of the position monitors.
  Reproducibility of the LHC circumference.
  1 Hz  10 mm.
Mode | Main difficulty | Favored for…
pp + PbPb | p and Pb never present at the ‘same time’ Reproducibility of BPMs Reproducibility of LHC circumference | 450 GeV
pPb + Pbp | Systematic differences ring1-ring2 | 450 GeV, 4 TeV
The measurement is a lot easier at injection because one can switch from p to Pb (and back) on the time scales of minutes.

## Slide 22: Results: Proton – Pb82+ calibration at injection
From the 2010-2012 runs, the momentum calibration can be extracted ‘parasitically’.
  Accuracy of Df estimated to ~ ±5 Hz.
Transporting a p-ion calibration of the SPS (450 GeV) to the LHC one obtains a consistent result:
Weighted average:
Run | Mode | Df (Hz) | P (GeV/c)
2010 | pp & PbPb | 4652 | 449.90 ± 0.35
2011 | pp & PbPb | 4638 | 450.58 ± 0.35
2012 | pPb | 4645 | 450.25 ± 0.35
Magnetic model:
450.00 ± 0.45 GeV/c

## Slide 23: Results: Proton – Pb82+ calibration at 3.5/4 Z TeV
p-Pb ramp test in October 2011:
  estimate for the momentum at 3.5 Z TeV.
p-Pb pilot physics fill of 2012:
  estimate for the momentum at 4 Z TeV.
In both cases the accuracy is limited by the uncertainty on orbit / RF frequency.
  Estimated uncertainty on the difference: ±4 Hz.
  There are good chances that we can improve the error in 2013 using both p-Pb and Pb-p data. Can be obtained largely parasitically.
Run | Df (Hz) | P (TeV/c)
2011 | 78.0 | 3.47 ± 0.10
2012 | 61.3 | 3.92 ± 0.13

## Slide 24: Magnet measurements
As an alternative to a direct measurement of the flat top energy, one could extrapolate 450 GeV measurements.
The expected accuracy on the momentum (dipole contribution) from the magnetic model is:
  Absolute field ~ 0.1%
  Relative field < 0.1%  Assume 0.1%
Interpolated energies:
  Uncertainties from tides and orbit corrector settings are included.
  Magnetic model error contribution dominates.
Run | E (GeV)
3.5 TeV | 3502 ± 5
4 TeV | 4002 ± 5
Excellent accuracy,
but not a direct measurement !

## Slide 25: Summary
Energy calibration at the LHC can be performed by comparing ion and proton frequencies.
  Good prospects at low energy, very challenging at 3.5-7 TeV.
The momentum measurement at 450 GeV is consistent with the magnetic model to better than 0.1%.
  Magnetic model accuracy confirmed at injection.
  LEP experience: 0.1-0.2% from good magnetic models is a realistic estimate of the error.
Currently the energy errors at 3.5-4 TeV are large, ~100 GeV. It should be possible to reduce the errors during p-Pb operation.
  Results available in February.
  Current results consistent with magnetic model.
Extrapolation of the 450 GeV measurements using the magnetic model will most likely provide smaller errors.
  But it is not a direct measurement.

## Slide 27: Polarization measurement @ LEP
Collide a laser pulse with circular polarization with the beam.
Inversion of the laser polarization leads to a vertical shift of the scattered photons (GeV energies), proportional to the vertical beam polarization.